Εργαστήριο Μικροϋπολογιστών
Θοδωρής Παπαρρηγόπουλος
el18040
Ομάδα 21

1ο Εργαστήριο στον 8085

Άσκηση 1

; x is C
; My counter is on D

LXI B,1000H ;1000 miliseconds delay

START:
MVI D,00H

GET_X:
LDA 2000H ; Read input
MOV H,A ; Store H
ANI 80H

JZ GET_X ; If msb is not on read again
;; Split C into X

MOV A,H
ANI 0FH ; 0000 1111 To get lsb's
MOV H,A

CPI 00H ; If input was 0 then jump to start
JZ START

INR H
JMP INCREASE

INCREASE:
;; check for msb
LDA 2000H
ANI 80H
JZ INCREASE

MOV A,D ; Get counter
CMA
OUT 30H
CALL DELB

INR D	; increase counter
MOV A,D
CMP H ; compare counter and x+1
JNZ INCREASE ; If not x+1 continue
DCR D ; get it to x

JMP DECREASE ; else decrease

DECREASE:
;; check for msb
LDA 2000H
ANI 80H
JZ DECREASE

DCR D
MOV A,D
CMA
OUT 30H
CALL DELB

MOV A,D
CPI 00H
JNZ DECREASE
INR D
JMP GET_X

END

Άσκηση 2

IN 10H

START: ;initializations
MVI A,10H ;space to print
LXI D,0B00H ; read dcd from here
STA 0B03H ;space
STA 0B04H ;space
STA 0B05H ;space
MVI A,00H
STA 0B02H ;initialize to 0

CALL KIND ;read 1st value
RLC
RLC
RLC
RLC ;16*x
MOV C,A

CALL KIND ;read 2nd value
ADD C ;16*x+y
MOV C,A
CPI C8H ;compare with 200
JC STATE_LESS_200 ;if smaller
;; We are in 2xx
MVI A,02H ; else print 2 in 3rd digit
STA 0B02H
MOV A,C
SUI C8H ;sub 200 to find decs -> 2xx - 200
JMP DECA

STATE_LESS_200:
CPI 64H ;compare with 100
JC DECA ;if less than 100
;; 3rd digit should be 1
MVI A,01H
STA 0B02H

MOV A,C
SUI 64H ;subract 10

DECA: ;hex to bcd
MVI B,FFH ;; 255 (MAX value)

DECS:
INR B
SUI 0AH
JNC DECS
ADI 0AH
STA 0B00H
MOV A,B
STA 0B01H

CALL STDM
CALL DCD ;print 3 digit decimal number
JMP START
END

Άσκηση 3

;; We have a counter that we are gonna
;; rotate left and right accordingly
;; It's important to notice that when lsb gets off
;; in 1000 0000 since there is a double switch, it should
;; continue with 0000 0001
;; same thing applies to 0000 0001 when you lsb gets off

LXI B,1000H ;1000 miliseconds delay

START:
MVI D,01H ; initialize B with 1
MVI L,00H ; L is the previus position of lsb

LEFT_CHECK:
IN 20H
MOV H,A
ANI 80H
JZ LEFT_CHECK ;; If msb is not on stay where you are

MOV A,H ; Move back H
ANI 01H ; Keep only lsb
CMP L
JZ LEFT
MOV L,A
CPI 00H
JZ RIGHT_CHECK

JMP LEFT

LEFT:
;; Rotate left, print
;; from 1000 0000 -> 0000 0001 we jump back to right
CALL DELB
MOV A,D
CMA
OUT 30H
CMA
RLC
MOV D,A
CPI 01H
JNZ LEFT_CHECK
RRC
JMP RIGHT_CHECK

RIGHT_CHECK:
IN 20H
MOV H,A
ANI 80H
JZ RIGHT_CHECK ;; If msb is not on stay where you are

MOV A,H ; Move back H
ANI 01H ; Keep only lsb
CMP L
JZ RIGHT
MOV L,A
CPI 00H
JZ LEFT_CHECK

JMP RIGHT

RIGHT:
CALL DELB
MOV A,D
RRC
CMA
OUT 30H
CMA
MOV D,A
CPI 01H
JNZ RIGHT_CHECK
RLC
JMP LEFT
END